## Slide 1: A Systematic Review on Long-Term Localization and Mapping for Mobile Robots
Ricardo B. Sousa, Héber M. Sobreira, António Paulo Moreira
Location of the presentation / Context
Month Day, Year

## Slide 2: Outline
Introduction
PICO Framework
Methodology
Results Overview
Discussion
Challenges and Future Directions
Conclusions

## Slide 3: Outline
Introduction
  Context
  Motivation
  Goals
PICO Framework
Methodology
Results Overview
Discussion
Challenges and Future Directions
Conclusions

## Slide 4: Introduction: Context
Autonomous mobile robot requires an environment representation
Simultaneous Localization and Mapping (SLAM)
  Robot pose estimation
  Mapping the environment

## Slide 5: Introduction: Context
Autonomous mobile robot requires an environment representation
Simultaneous Localization and Mapping (SLAM)
  Robot pose estimation
  Mapping the environment
Static scene only requires mapping once the environment
Real world is not static!
  Moving elements
  Environment reconfiguration
  Appearance variations

## Slide 6: Introduction: Context
Autonomous mobile robot requires an environment representation
Simultaneous Localization and Mapping (SLAM)
  Robot pose estimation
  Mapping the environment
Static scene only requires mapping once the environment
Real world is not static!
  Moving elements
  Environment reconfiguration
  Appearance variations
How and when to update the map
  Consider most current state, only static?
  Update when changes occur, after certain time?

## Slide 7: Introduction: Context
Autonomous mobile robot requires an environment representation
Simultaneous Localization and Mapping (SLAM)
  Robot pose estimation
  Mapping the environment
Static scene only requires mapping once the environment
Real world is not static!
  Moving elements
  Environment reconfiguration
  Appearance variations
Limited computational resources
  Indefinitely growth of the map
How and when to update the map
  Consider most current state, only static?
  Update when changes occur, after certain time?

## Slide 8: Motivation
Several existent studies overview SLAM literature
  Past, present, and future of simultaneous localization and mapping: Toward the robust-perception age (2016)
  Simultaneous localization and mapping: A survey of current trends in autonomous driving (2017)
  …

## Slide 9: Motivation
Several existent studies overview SLAM literature
  Past, present, and future of simultaneous localization and mapping: Toward the robust-perception age (2016)
  Simultaneous localization and mapping: A survey of current trends in autonomous driving (2017)
  …
However,
  No overview on challenges related to long-term SLAM
  No clear methodology for selecting the papers

## Slide 10: Goals
Systematic Literature Review (based on PRISMA)
Bibliographic analysis
  Keywords co-occurrence
  Co-authorship
Focus on challenges related to long-term SLAM
  Appearance variance
  Environment dynamics
  Map sparsification
  Multi-session
  Computational concerns

## Slide 11: Goals
Analysis on the experimental data used in the literature
  Public datasets
  Environment conditions
  Sensory setup
  Distance and time properties
Evaluation metrics

## Slide 12: Outline
Introduction
PICO Framework
Methodology
Results Overview
Discussion
Challenges and Future Directions
Conclusions

## Slide 13: PICO Framework
Population – Intervention – Comparison – Outcome (PICO)
PICO as a template for the review’s topic

## Slide 14: PICO Framework
Population: mobile robots
Intervention: localization, mapping, SLAM
Comparison: not applicable
Outcome: long-term operation, lifelong autonomy, robust

## Slide 15: Outline
Introduction
PICO Framework
Methodology
  Search & Selection
  Data Extraction
Results Overview
Discussion
Challenges and Future Directions
Conclusions

## Slide 16: Methodology: Search & Selection
Search base string
(robot* OR vehicle*) AND
((locali* AND map*) OR “slam”) AND
(“long term” OR “life long” OR
lifelong)
Last full inquiry on May 17, 2022

## Slide 17: Methodology: Search & Selection
Search base string
(robot* OR vehicle*) AND
((locali* AND map*) OR “slam”) AND
(“long term” OR “life long” OR
lifelong)
Last full inquiry on May 17, 2022
Selection Process
  Identification
  Screening
  Quality Assessment
Fig. 1: PRISMA flow diagram for the selection process

## Slide 18: Data Extraction
Long-term considerations
Localization
Mapping
Multi-robot
Execution mode
Environment and domain
Sensory setup
Non-public experiments?
Ground-truth
Distance and time
Datasets
Evaluation metrics

## Slide 19: Data Extraction
Long-term considerations
Localization
Mapping
Multi-robot
Execution mode
Environment and domain
Sensory setup
Non-public experiments?
Ground-truth
Distance and time
Datasets
Evaluation metrics
Further details available in the preprint…

## Slide 20: Outline
Introduction
PICO Framework
Methodology
Results Overview
  Keywords Co-occurrence
  Co-authorship Analysis
Discussion
Challenges and Future Directions
Conclusions

## Slide 21: Results Overview: Keywords Co-occurrence
Fig. 2: Keywords co-occurrence analysis on the 142 included records generated by VOSviewer with overlay visualization by the average publication year

## Slide 22: Co-authorship Analysis
Fig. 3: Co-authorship analysis on the 142 included records generated by VOSviewer

## Slide 23: Outline
Introduction
PICO Framework
Methodology
Results Overview
Discussion
  Appearance Invariance
  Dynamics Modeling
  Map Sparsification
  Multi-Session
  Computational
  Long-Term Experimental Data
  Evaluation Metrics
Challenges and Future Directions
Conclusions

## Slide 24: Discussion: Appearance Invariance
Experience maps
  Topological maps
  Experience ~ view of the environment
  Invariance ~ accumulated knowledge
  Possible application on Visual Teach & Repeat (VT&R) systems
  Not scalable in dynamic environments
Fig. 4: Spatiotemporal pose graph data structure used to represent a multi-experience network of paths in a VT&R system
Source: K. MacTavish, M. Paton, T.D. Barfoot: Selective memory: Recalling relevant experience for long‐term visual localization (2018). Journal of Field Robotics, 35(8), pp. 1265–1292. doi: 10.1002/rob.21838

## Slide 25: Appearance Invariance
Illumination transformations
  Preprocessing process
  Applied to color images
  Increase invariance on changing lightning conditions
  Examples
    Illumination invariant space
    Learning transformations
    Gamma correction
Fig. 5: Example of using the illumination invariant space for place recognition
Source: Z. Yang, Y. Pan, L. Deng, Y. Xie, R. Huan: PLSAV: Parallel loop searching and verifying for loop closure detection (2021). IET Intelligent Transport Systems, 15(5), pp. 683–698. doi: 10.1049/itr2.12054

## Slide 26: Appearance Invariance
Handcrafted features
  Keypoint detector + descriptor computation
  Visual features
    Position Invariant Robust Features (PIRF) ~ only select stable local features
    Capture gradient information for improve seasonal invariance
      Histogram of Oriented Gradients (HOG)
      Local Difference Binary (LDB)
    2D/3D laser point cloud > 2D image representation > feature extraction
      Similar for radar sensor data
  Environment structure features
    Lines, corners, edges, planes
    Ceiling salient edge points
    Poles

## Slide 27: Appearance Invariance
Convolutional Neural Networks (CNN)
  CNN-based features more discriminative than handcrafted ones
  CNN feature maps
    Local features
    Place recognition as classification task
    Geometry cues in lower levels vs semantic information in higher levels
    Not only image data, also 3D LiDAR and radar place recognition
  Semantic segmentation
  Appearance-content disentanglement
Fig. 6: Overview of the VGG16 architecture to exemplify feature maps retrieved from different layers
Source: Z. Yang, Y. Pan, L. Deng, Y. Xie, R. Huan: PLSAV: Parallel loop searching and verifying for loop closure detection (2021). IET Intelligent Transport Systems, 15(5), pp. 683–698. doi: 10.1049/itr2.12054

## Slide 28: Appearance Invariance
Convolutional Neural Networks (CNN)
  CNN-based features more discriminative than handcrafted ones
  CNN feature maps
  Semantic segmentation
    Stable features
    Pixel-wise segmentation
    Graph embedding of semantic features
    Applicable to other sensors (3D LiDAR)
  Appearance-content disentanglement
(not possible to show examples due to require payment of copyright fees…)

## Slide 29: Appearance Invariance
Convolutional Neural Networks (CNN)
  CNN-based features more discriminative than handcrafted ones
  CNN feature maps
  Semantic segmentation
  Appearance-content disentanglement
    Image ~ appearance + content
    Use content features to improve appearance invariance
    Encoder-decoder-based networks
Fig. 7: Variational Autoencoder for appearance-content disentanglement
Source: J. Oh, G. Eoh: Variational Bayesian Approach to Condition-Invariant Feature Extraction for Visual Place Recognition (2021). Applied Sciences, 11(19), pp. 8976. doi: 10.3390/app11198976

## Slide 30: Appearance Invariance
Feature stability
  Predictor functions (#observations, concentration ratio, …)
  Consecutive observations, observation time
Multi-modal features
  Multi-modal as more discriminative than single feature spaces
Image sequence matching
  Temporal coherence of visual data
Sensor modalities
  Instead of image-only, consider 2D/3D lasers, radar, thermal, depth, …

## Slide 31: Dynamics Modeling
Map representation
  Short/Long-Term Memory (S/LTM)
    Multi-store model of human memory
    Multiple timescales
    Use LTM maps for localization
  Static vs dynamic maps
Fig. 8: Multi-store model of human memory proposed by Atkinson
and Shiffrin (1968)
Source: https://commons.wikimedia.org/wiki/File:Memory_multistore_model.svg

## Slide 32: Dynamics Modeling
Map representation
  Short/Long-Term Memory (S/LTM)
  Static vs dynamic maps
    Identification of moving elements
    Distinction between static – semi-static – dynamic changes
    Ignore dynamic elements for static map
    Use static map for localization
(not possible to show examples due to require payment of copyright fees…)

## Slide 33: Dynamics Modeling
Map matching
  Observation vs map
  Clustering properties of observations
  Ray tracing
  NDT + occupancy grid map hybrid representation

## Slide 34: Dynamics Modeling
Prediction modeling
  Markov-based processes
    State holding time associated to Markov processes
  Patterns periodicity
    Fourier analysis
    Time series as stationary stochastic processes
  CNN-based prediction

## Slide 35: Dynamics Modeling
Dynamic objects detection
  Assume certain semantic classes as dynamic
  Use features associated to static objects for localization and mapping
  Bounding box segmentation (YOLO)
  Pixel-wise segmentation

## Slide 36: Map Sparsification
Ever growing problem of continuously performing SLAM
Pose graph SLAM
  Mutual information between nodes
  Outdated information of sensor observations
  Nodes’ spatial density and time recency
  Information fusion
  Also appliable to Keyframe SLAM

## Slide 37: Map Sparsification
Features management
  Spatial distribution
  Matching observations vs number of attempts
  Predictor functions (#observations, concentration ratio, …) to evaluate feature stability
  Merge ambiguous information

## Slide 38: Multi-Session
Global multi-session
  Common frame between all sessions
  Assume that localization always possible to perform in current map
Independent sessions
  Each run starts a new mapping session
  Offline / online processes try to formulate inter-session loop closures
Anchor nodes
  Representation of independent sessions in the same graph
  Each session has an associated anchor node
  Anchor node links a transformation from the global to the session’s frame

## Slide 39: Computational
Other challenges in addition to map sparsification
Map management
  RAM vs disk memory
  Geodetic quadtree tiling for Earth-scale mapping
Dimension reduction of feature descriptor
  Contributes for reducing the map size requirements
  Principal Component Analysis (PCA)
  Sparse Random Projection
  Max-pooling of CNN-based feature maps
  Semantic hashing

## Slide 40: Computational
Parallel computing
  Multi-thread/process computing
  External computation (cloud/edge devices

## Slide 41: Long-Term Experimental Data
Fig. 9: Evolution of the usage of public datasets per year considering the 142 included records in the review

## Slide 42: Long-Term Experimental Data
Public datasets
  89/142 (62.7%) included works use public datasets
  Examples
    Oxford RobotCar
    USyd Campus
    COLD
    …
Ground-truth data
  Manual (annotation/labelling, alignment)
  GPS
  External tracking systems (OptiTrack, Vicon)
  SLAM / laser-based data
  CAD

## Slide 43: Evaluation Metrics
Place recognition
  Precision-recall metrics
  F-score, F-beta
  Confusion matrix
Robot pose
  Mean, standard deviation, Root Mean Square Error (RMSE)
  Absolute Trajectory Error (ATE)

## Slide 44: Evaluation Metrics
Map sparsity
  Map size (#nodes, #edges, #features)
  Kullback-Leibler Divergence (KLD) for pose graph SLAM
Computational performance
  Execution time
  Memory
  Computational complexity (O(N), …)

## Slide 45: Outline
Introduction
PICO Framework
Methodology
Results Overview
Discussion
Challenges and Future Directions
Conclusions

## Slide 46: Challenges and Future Directions
Vision-based global place recognition
  Omnidirectional vision
  Data augmentation

## Slide 47: Challenges and Future Directions
Vision-based global place recognition
Dynamics modeling
  Definition of environment dynamics
  Account dynamics in both localization and mapping

## Slide 48: Challenges and Future Directions
Vision-based global place recognition
Dynamics modeling
Online graph sparsification
  Online sparsification
  Sparsification in highly dynamic environments

## Slide 49: Challenges and Future Directions
Vision-based global place recognition
Dynamics modeling
Online graph sparsification
Decentralized computation
  Application of decentralized computation in long-term localization and mapping
  External compute agents (edge/cloud devices) for off-loading computation tasks

## Slide 50: Challenges and Future Directions
Vision-based global place recognition
Dynamics modeling
Online graph sparsification
Decentralized computation
Multi-robot long-term SLAM
  Decentralized and distributed SLAM execution
  Heterogeneous robots

## Slide 51: Challenges and Future Directions
Vision-based global place recognition
Dynamics modeling
Online graph sparsification
Decentralized computation
Multi-robot long-term SLAM
Active exploration
  Active navigation to improve long-term performance of SLAM algorithms

## Slide 52: Challenges and Future Directions
Vision-based global place recognition
Dynamics modeling
Online graph sparsification
Decentralized computation
Multi-robot long-term SLAM
Active exploration
Human-to-Machine Interfaces (HMI)
  User provide information on environment dynamics/changes
  Usage of high-level geometric and semantic features to interact with the end-user

## Slide 53: Outline
Introduction
PICO Framework
Methodology
Results Overview
Discussion
Challenges and Future Directions
Conclusions

## Slide 54: Conclusions
Appearance variance
  CNN-based features more discriminative than handcrafted ones
  Geometric/semantic cues more robust than appearance ones

## Slide 55: Conclusions
Appearance variance
  CNN-based features more discriminative than handcrafted ones
  Geometric/semantic cues more robust than appearance ones
Environment dynamics
  Static – semi-static – dynamic identification most common approach
  Usage of static permanent changes for localization

## Slide 56: Conclusions
Appearance variance
  CNN-based features more discriminative than handcrafted ones
  Geometric/semantic cues more robust than appearance ones
Environment dynamics
  Static – semi-static – dynamic identification most common approach
  Usage of static permanent changes for localization
Map sparsification
  Goal: constrain map size to explored environment area
  Mutual information rejection

## Slide 57: Conclusions
Appearance variance
  CNN-based features more discriminative than handcrafted ones
  Geometric/semantic cues more robust than appearance ones
Environment dynamics
  Static – semi-static – dynamic identification most common approach
  Usage of static permanent changes for localization
Map sparsification
  Goal: constrain map size to explored environment area
  Mutual information rejection
There are still open challenges on long-term SLAM

## Slide 58: Any questions?
Corresponding author: Ricardo B. Sousa
up201503004@edu.fe.up.pt

## Slide 59: A Systematic Review on Long-Term Localization and Mapping for Mobile Robots
Ricardo B. Sousa, Héber M. Sobreira, António Paulo Moreira
Location of the presentation / Context
Month Day, Year

## Slide 60: References
R.B. Sousa, H.M. Sobreira, A.P. Moreira: A Systematic Review on Long-Term Localization and Mapping for Mobile Robots (2022). DOI: 10.22541/au.166739295.55264285/v1
C. Cadena et. al.: Past, present, and future of simultaneous localization and mapping: Toward the robust-perception age (2016). IEEE Transactions on Robotics, 32(6), pp. 1309–1332. DOI: 10.1109/TRO.2016.2624754
G. Bresson et. al.: Simultaneous localization and mapping: A survey of current trends in autonomous driving (2017). IEEE Transactions on Intelligent Vehicles, 2(3), pp. 194–220. DOI: 10.1109/TIV.2017.2749181
M.J. Page et. al.: PRISMA 2020 explanation and elaboration: Updated guidance and exemplars for reporting systematic reviews (2021). BMJ, 372(160). DOI: 10.1136/bmj.n160
M. Borrego, M.J. Foster, J.E. Froyd: Systematic Literature Reviews in Engineering Education and Other Developing Interdisciplinary Fields (2014). Journal of engineering education, 103(1), pp. 45–76. DOI: 10.1002/jee.20038